## Slide 1: シンチレータストリップを用いた 高性能電磁カロリメータの開発
（公募研究Ａ１）
研究代表者 川越清以 (神戸大学)
with the GLC calorimeter group
(KEK, Kobe, Konan, Niigata, Shinshu, Tsukuba)
9-Mar-2004, 科研費特定領域 第2回研究会 in Tsukuba
(Special thanks to Dr. Matsunaga)
Introduction
Hardware study with test beams
Photon sensors
Simulation study
Future plan
Summary

## Slide 2: Introduction
Design criteria for LC calorimeter
  good energy resolution for single particles
  fine transverse/longitudinal granularity for “particle flow” analysis
  hermeticity
  operational in strong magnetic field
Required performance
  2-jet mass resolution better than W/Z natural width

## Slide 3: Our approach to the design criteria
Baseline design :
Lead/plastic scintillator sampling calorimeter for both ECAL and HCAL
  Hardware compensation for excellent hadron energy resolution and linearity
  Good hermeticity
  Good granularity
  Established technology and reasonable cost
  According to fast simulation, this conservative design can fulfill design criteria
Reconstructed W mass for e+e-->W+W- at 400GeV
(result of fast simulation in which ECAL cell size was 10cm)
(Mjj) = 2.9GeV

## Slide 4: Our previous studies
Study on energy resolution and linearity
  Test beam measurements at KEK and FNAL
    ECAL with 4mm-Pb/1mm-Sci :
    for electrons
    HCAL with 8mm-Pb/2mm-Sci /2mm-Acryl :
for pions
Tile/fiber calorimeter with hardware compensation has been verified to meet our design criteria for energy resolution and linearity even with current design of granularity
  Detailed simulation study must be done

## Slide 5: HCAL studies with test beam (1996-1999)
Good energy resolution and linearity thanks to hardware compensation

## Slide 6: Fine granularity ECAL
Currently studying fine granularity ECAL with Pb/Sci sampling technique
  examine “particle flow” analysis capability
Baseline design : tile/fiber ECAL
  4cmx4cmx1mm-Sci + 4mm-thick Pb
Optional design : strip-array ECAL
  1cmx20cmx2mm-Sci + 4mm-thick Pb
Shower-max detector with scinti-strips
  Conventional WLS readout
  Directly-attached APD readout
Require multi-channel photon sensors operational in magnetic field

## Slide 7: Purposes of test beam studies
(1) Tile/fiber ECAL
  examine uniformity with staggerd WLS layouts
(2) Strip-array ECAL
  uniformity measurement for the simulator inputs
  measure energy, position, shower direction
  examine 2-cluster separation and ghost-rejection
(3) WLS-readout SHmax
  position resolution
  e/ separation
(4) Direct-APD SHmax
  examine feasibility : S/N for MIP signal
  position resolution

## Slide 8: Test beams for new ECAL design
2002 Nov.: T517 at KEK (e//, 1-4 GeV)
  tile/fiber ECAL, strip-array ECAL, scinti-strip SHmax
2003 Sept.: test at DESY (e, 1-6 GeV)
  scinti-strip SHmax
2004 March: T545 at KEK (e//, 1-4 GeV)
  tile/fiber ECAL, strip-array ECAL, scinti-strip SHmax
  probably the last opportunity for KEK PS beamline
Setup of T517 test beam measurement

## Slide 9: (1) Tile/fiber ECAL
Small cell size of 4cm x 4cm, 0.7mm-WLS
Effect of small bending radius of WLS fiber ?
Non-uniformity (around tower boundary) ?
Only 2 super layers (2002)
Full-depth, mega-tiles (2004)
Multi-anode PMTs

## Slide 10: WLS fiber configuration
Roundish-square groove layout
Circular groove layout
Two types of groove layout to smear non-uniformity

## Slide 11: Non-uniformity measurements
Better uniformity with alternating layout

## Slide 12: Spatial resolution
Position resolution of 2nd S.L.
(x or y) ~ 0.7cm at 4GeV
as a function of beam energy

## Slide 13: (2) Strip-array ECAL
Full-depth test module was constructed and tested in 2002
24 layers (17X0), 6 super-layers
1 layer = lead plate (4mm-thick) + x-strips + y-strips
20cm x 1cm x 2mm scinti-strip with 1mm-WLS
Multi-anode PMTs (tentatively for beam test)

## Slide 14: Energy resolution
Test beam
GEANT3 simulation
w/o photon statistics
If photon statistics is taken into account, beam test results are consistent with simulation.

## Slide 15: Linearity
Linearity : < 3.5%
  < 1% above 2GeV
  deviation at 1GeV : due to material in front of ECAL ?
In good agreement with simulation

## Slide 16: Spatial resolution
Position resolution for 4GeV electron
=2.0mm
around shower max
A 4GeV electron event : Fitted to Gaussian

## Slide 17: Angle measurement
Shower-axis angle is determined by linear fitting points in the first 5 S.L.
Mean S.L. position in beam direction is calculated with weighted mean of energy deposit obeying shower curve

## Slide 18: Angle measurement (cont.)
Offset due to mis-alignment ?
Ignoring offset, angles are correctly measured within errors
Incident angle : 0 ~ 3 degree

## Slide 19: Response uniformity
Response in 1st super layer for 2Gev  and e
Response-sum over strips : uniformity < 5%

## Slide 20: 2-particle separation / ghost rejection
For strip-array ECAL, ghost must be rejected
  pulse height analysis could help for rejection
2-particle separation and ghost rejection : study in progress
2 cluster separation in 1-dim. (2nd S.L.)
particle
particle
ghost
ghost
3cm
4cm
1cm
2cm

## Slide 21: (3,4) Shower-max detectors
For tile/fiber ECAL case, position detector at shower maximum is needed for
  better position resolution
  better track-cluster matching
  good e/ separation capability
Scinti-strip detector is a natural option for our ECAL
  baseline design : WLS readout
  optional design : directly-attached APD

## Slide 22: Readout of scinti-strip
Strip-size :
  20cm x 1cm x 1cm
Conventional readout:
  WLS + clear fiber to
  MA-PMTs (tested)
  HPDs (2004)
Directly-attached APDs on scinti-strip (tested)
SiPMs directly on WLS (2004)

## Slide 23: SHmax test modules
Scinti-strips with WLS fibers
Scinti-strips with directly attached APDs

## Slide 24: (3) Position resolution of SHmax (WLS read out)
xSM(cm)
corrected
xSM(cm)
Before S-shape correction
After S-shape correction
xDC(cm)
xDC(cm)
xSM-xDC(cm)
xSM-xDC(cm)
 = 1.9mm
 = 1.7mm
XSM : measured position with Gaussian fit
XDC : incident position determined by drift chambers
6 GeV electrons
(DESY)

## Slide 25: Position resolution of SHmax (cont.)
vs. electron energy
vs. Pb thickness in front
Electron incident position is determined with weighted mean of 5 strips for figures below:
Electron energy (GeV)
Pb thickness (mm)
Position resolution （cm）
Position resolution （cm）
Pb thickness = 24cm
2GeV e
6GeV e

## Slide 26: (4) Performance of APD-SHmax
MIP signal is well separated from pedestal
ADC count
APD : Hamamatsu S8864-55
  Active area : 5mm x 5mm, gain ~ 50
  Temperature coefficient : ~5%/degree corrected
Spatial resolution as a function of electron energy
Weighted mean method

## Slide 27: Photon sensors
Multi-pixel Hybrid Photodiode (HPD)
  DEP-HPD used for CMS-HCAL
  We have tested Hamamatsu 64 pixels HAPD (Dr. Suyama)
    Gain = 6 x 104 (good)
    Commercially not yet available
Electron-bombarded CCD (EBCCD)
  Suitable for fiber readout
  ～400 fibers/device possible
  Low gain (< 1000), but
  Sensitivity to single-photon
  Slow read out, no timing information
Will be tested with SHmax in 2004 test beam

## Slide 28: Photon sensors (cont.)
SiPM
  Micro-APD cells operated in Geiger mode
  1ch/device, compact, cheap (a few $/device)
  High gain (~106), but significant noise rate
  Can be directly attached to WLS fiber
  ~10 SiPM from DESY to be tested in 2004 beam test
  HPK is developing a similar photon sensor

## Slide 29: Simulation studies
Implemented geometry for both options of ECAL into GEANT3-based full simulator
  Detailed studies, such as shower clustering and track-cluster matching, are still under study
Will move to GEANT4-based simulation
  Basic implementation is done; need more refinement
Behind schedule due to insufficient man power and need to do beam test before KEK-PS shutdown

## Slide 30: Future plan
Finalize ECAL hardware study in 2004
Accelerate simulation studies
  Full simulation in GEANT4 framework
  Jet clustering
Continue to study photon sensors
  SiPM, HPD, EBCCD….
International collaboration : photon sensors, scinti. production, …
Engineering study

## Slide 31: Summary
Fine granularity ECAL based on lead/scintillator sampling is being studied :
  established technology, reasonable cost
  energy resolution, linearity, hermeticity
  a series of beam tests is being carried out: tile/fiber ECAL, strip-array ECAL, SHmax Final beam test starts soon.
  new photon sensors are being tested
  simulation studies are in progress