## Slide 1
赤外線観測ロケット実験による宇宙背景ニュートリノ崩壊探索実験
武内 勇司（筑波大素粒子実験グループ）
「背景放射で拓く宇宙創成の物理
－インフレーションからダークエイジまで－」シンポジウム2012
2012年7月26日
高エネルギー加速器研究機構研究本館小林ホール

## Slide 2: Motivation
物理背景
  ニュートリノ崩壊現象の探索
    ニュートリノ遷移輻射光の検出 (ν3→ν2,1+γ)
  宇宙背景ニュートリノ(~110個/cm3/世代，T=1.95K）を利用
    逆にニュートリノ崩壊光の観測宇宙背景ニュートリノの発見
  と仮定すると（λ=50μm）
    の直接測定
標準理論
L－R対称模型（U(1)SU(2)L SU(2)R）のモデル
  まで短くなる可能性()
二体崩壊なのでの重心系では，モノクロ光
1.9Kの速度分布＋赤方偏移の影響

## Slide 3: 信号検出の可能性
CIB (COBE)
検出器のエネルギー分解能
0%
1%
3%
2%
望遠鏡：20cm径，0.1°の集光
測定時間：10時間
検出効率100％，エネルギー分解能2%で一光子ごとのエネルギー測定が可能な検出器を仮定
6.7σで観測可能
宇宙赤外線背景輻射
（前景放射を含まず）
+
ニュートリノ崩壊光の分布
(, yr)
25meV (λ=５０μm)

## Slide 4: COBEとAKARIの宇宙赤外線背景輻射の測定結果
COBE: M. G. Hauser et al.Astrophys. J. 508 (1998) 25.
D. P. Finkbeineret al.Astrophys. J. 544 (2000) 81.
AKARI: S. Matsuura et al.Astrophys. J. 737 (2011) 2.
50meV
25meV
10meV

## Slide 5: AKARIデータを用いた寿命下限値の評価
x1012 yr
AKARIで測定されたCIBをすべてニュートリノ崩壊にからの寄与だと仮定
の関数として求めたの寿命の下限値
JPSJの論文としてPublished(2012年1月)

## Slide 6
赤外線観測ロケットによる宇宙背景ニュートリノ崩壊探索の計画
回折格子+Nb/Al-STJの組み合わせによる赤外光子エネルギー測定器
  λ＝40～80μm (
  Nb/Al-STJのアレイ
    Nb/Al-STJの一つのセルは，非常に良いS/NのEγ～25meVのフォトンカウンティング検出器として使用
    Nbの超伝導エネルギーギャップ: 17 electrons/25meV
  極低温2K前置増幅器の開発
    Nb/Al-STJで10~20electron×trapping増幅の信号出力
    フェルミラボとのコラボレーション(日米科学技術協力事業)
STJ array
50pixel x 8 row

## Slide 7: 日米協力事業で2012年度から「ニュートリノ崩壊探索」
共同研究者リスト （2012年3月）
Japan Group
Shin-Hong Kim, Yuji Takeuchi, Ken-ichi Takemasa, Takashi Onjo,
Hyun-Sang Jeong, Shinya Kanai, Kazuki Nagata (University of Tsukuba) ,
Hirokazu Ikeda, Shuji Matsuura (JAXA/ISAS) ,
Hirokazu Ishino, Atsuko Kibayashi, Satoshi Mima,
Yasuki Yuasa(Okayama University) ,
Takuo Yoshida, Yusuke Shimizu, Mikiya Nagashima (Fukui University) ,
Yukihiro Kato (Kinki University) ,
Masashi Hazumi (KEK)
US Group
Erik Ramberg, Jonghee Yoo, J. C. Estrada (Fermilab)
Korea Group
Soo-Bong Kim (Seoul National University)

## Slide 8: CIB Experiment for Neutrino Decay Search with JAXA Rocket
Secondary
mirror
Main
Mirror
15cmΦ
F=1m
Focal plane
Instruments
Liq-He tank
1.7K
>1W
Grating
Tertiary
mirror
Superconducting
Tunnel Junction
(STJ) Detector Array
(50 x 8 channels)
Focal plane
Instruments
IR Light
Preamplifiers(2K)
5 minutes DAQ at 200km height in 2016
50cm
Post-Preamplifier
DAQ system
1.7K Cryostat
>1W
Star Sensor
Vibration
Damper
120cm
Weight 100kg

## Slide 9: CIB Experiment for Neutrino Decay Search with JAXA Rocket Focal Plane Instruments
Grating
Tertiary
mirror
STJ Detector Array
(50 x 8 channels)
Focal plane Instruments
Preamplifier(2K)
d=1mm
Grating
m = 0
m = 1
Δλ＝1μm

D=10cm
x=5mm
Δx=100μ
50pixels
8pixels
Field of View ＝20” x 2.7’
1pixel: 20” x 20” , 1 spectrometer: 50 pixels
λ＝40～80μm (
Rate/50pixels= 0.7kHz at 40μm

## Slide 10: CIB Experiment for Neutrino Decay Search with JAXA Rocket Rate Calculation and Expected Lifetime Limit
Rate/pixel = 0.7kHz at λ＝ 40μm
Measurements for 200 s
→ 140 k events /pixel 8 row
=1120k events/photon energy
黄道光（前景放射）
系外銀河
第一世代の星?
背景放射
CMB
DGL
FIR-rocket
Photon数の統計エラーのみだとすると
での測定が可能
(CIBの寄与～)
先の論文よりもニュートリノ寿命の下限値をオーダー以上改善可能
λ＝40～80μm

## Slide 11: Nb/Al-STJ R&D status 可視光域(青色)DC光レーザーに対する応答
美馬氏（理研）作成@KEKを使用
パルスレーザーを高周波数で点灯(DC光源として使用）
  f = 1MHz
  /pulseO(104) (不定性大)
I-V curve of Nb/Al-STJ sample
laser off
laser on
1MHz,~104photons
T100mK, 磁場あり
V

## Slide 12
入射光源
大光量レーザーパルスを10MHzで30パルス(計3μs)
Nb/Al-STJ R&D status 可視光域(青色）パルス光レーザーに対する応答
Pre-Amp
Ortec147c
Shaper
STJ
Vbias=1mV
/pulseO(104) (不定性大)
40μs/DIV

## Slide 13: まとめ
赤外線宇宙背景放射の測定によるニュートリノ崩壊探索実験の可能性
回折格子() ＋Nb/Al-STJを検出器とするCIB観測ロケット実験を計画中
  ニュートリノ寿命の下限をより厳しく与える．CIB（ ）の精密測定
  Nb/Al-STJによる遠赤外域光子のフォトンカウンティングの実現が必要
  Nb/Al-STJの光応答のテスト，超低温(2K)プリアンプの開発が進行中
  STJ/Pre-ampの多チャンネル化，ロケット実験用光学系，冷却系，DAQなどR&Dが必要

## Slide 14: BACKUP

## Slide 15: CIB Experiment with JAXA Rocket in 1992
15
15
220km
338km
182km

## Slide 16: CIB Experiment with JAXA Rocket in 1992 NIR(近赤外線) Spectrometer
FOV（視野） 0.2°x 0.2°
λ＝1.4μ～4.1μ Δλ＝0.13μ
InSb半導体検出器：
ギャップエネルギー 0.17eV
（λ＝7.9μ）
20 x 2 pixels, 1mm x 0.5mm, 50pF
operated at 2K,
dark current < 50 e s-1
Charge-integrating amplifier at 7０K
1s read noise: 100 e

## Slide 17: CIB Experiment with JAXA Rocket in 1992 FIR(遠赤外線） Photometer
Ge:Ga半導体検出器： 非圧縮型（BC１）、圧縮型
圧縮型sensitivity < λof 200μ ( 6.7meV )
size 1 x 1 x 1.5 mm
CⅡ line
(FOV)
Winston Horn

## Slide 18: Specification of 2K preamplifier
Common specification: Operation temperature: ~2K
Integration time: 10 μsec <For the Nb/Al-STJ and Hf-STJ prototype design> Dynamic range < 20fC ( ~1.2 x 105 e)
from the requirement of < 4.5eV γ ( λ＝270 nm ) at HF-STJ Noise < 0.34 fC ( ~2100 e) from the requirement of < 2.5% for 13.4 fC = 3 eV γ (λ＝410 nm ) at Hf-STJ and of <20% for 1.6fC = 3 eV γ (λ＝ 410 nm ) at Nb/Al-STJ Gain: 40mV/fC （ 0.064V/1.6fC ) <For Nb/Al-STJ final design> Dynamic range < 0.064fC ( ~400 e)
from the requirement of < 300 meV γ at Nb/Al-STJ Noise < 0.0026 fC ( ~16 e) from the requirement of <20% for 0.013 fC = 25meV γ at Nb/Al-STJ Gain: 1V/fC （ 0.013V/0.013fC ) <For Hf-STJ final design> Dynamic range < 4.3fC ( ~27000 e) from the requirement of < 45meV γ at HF/W-STJ Noise < 0.012fC ( ~80e) from the requirement of <0.5% for 2.4 fC = 25meV γ at Hf/W-STJ Gain: 1V/fC （ 2.4V/2.4fC )

## Slide 19: Readout Electronics ( Post- Preamplifier )
Grating
Tertiary
mirror
Focal plane Instruments
2K Preamplifier
2K
Post-preamplifier
Superconducting
Tunnel Junction
(STJ) Detector Array
(50 x 8 channels)
Shaper
Discriminator
and Register
PC
+ Wireless
Data transfer
(100kbps)

## Slide 20: Schedule
20
20
Nb/Al-STJ設計・開発
 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Experiment Design |  |  |  |  |  | 
SuperconductingTunnel Junction (STJ ) Detector |  |  |  |  |  | 
Preamplifier at 2K and Post-Preamp (Fermilab, JAXA, Tsukuba） |  |  |  |  |  | 
Dispersive Element, Optics (JAXA, Tsukuba) |  |  |  |  |  | 
Cryostat ( JAXA, KEK) |  |  |  |  |  | 
Measurements＋Analysis （All） |  |  |  |  |  | 
Experiment with FIR Rocket
Experiment with Satellite such as SPICA
Design and R&D of Nb/Al-STJ Detector
Production
Production
Design and R&D
Simulation
Design and R&D
Design and R&D of Hf-STJ Detector
Production
Analysis Program
Analysis
Design and R&D
Production
Far-Infrared Observatory Rocket Experiment

## Slide 21: Plan
Design and detector R&D of CIB measurement with a FIR-rocket launched in 2016
Multi-cell Nb/Al-STJ (Tsukuba,Fukui,Okayama)
Low-temperature (2K) preamplifier and post-preamplifier (Fermilab, JAXA, Tsukuba)
Dispersive element such as grating (Tsukuba, JAXA)
Cryostat（1.7K) (JAXA)
2. Superconducting detector R&D for satellite CIB measurement after 2018
Multi-cell Hf-STJ development (Tsukuba, Fukui)