## Slide 1
R&D of cryogenic SOI amplifier for COBAND experiment Rena Wakasa (Univ. of Tsukuba)
for COBAND Collaboration
Shin-Hong Kim, Yuji Takeuchi, Takashi Iida, Kenichi Takemasa, Kazuki Nagata, Shunsuke Yagi, Chisa Asano, Rena Wakasa, Yoichi Otsuka (Univ. of Tsukuba), Hirokazu Ikeda, Takehiko Wada, Koichi Nagase (JAXA/ISAS), Shuji Matsuura (Kwansei gakuin Univ), Yasuo Arai, Ikuo Kurachi, Masashi Hazumi (KEK), Takuo Yoshida，Takahiro Nakamura, Sakai Makoto (Univ. of Fukui), Satoshi Mima (RIKEN), Kenji Kiuchi (Tokyo Univ.),
H.Ishino, A.Kibayashi (Okayama Univ.), Yukihiro Kato (Kindai University), Go Fujii, Shigetomo Shiki, Masahiro Ukibe, Masataka Ohkubo (AIST), Shoji Kawahito (Shizuoka Univ.), Erik Ramberg, Paul Rubinov,
Dmitri Sergatskov (Fermilab)， Soo-Bong Kim (Seoul National University)
COsmic BAckground Neutrino Decay search experiment
  The purpose of the experiment is to determine neutrino masses by measuring the neutrino decay photon.
  Neutrino has a long lifetime (T>O(1012) years : COBE+AKARI measurement). We use the cosmic background neutrino.
  The emitted photon energy from the diagram is It is expected at . We measure the energy by using the superconducting tunnel junction.
Number of created Quasi-particles
Energy Resolution
: Trapping Gain(~10)
: Energy of Incident Photon
: Energy Gap in Superconductor
: Fano Nactor
STJ(Superconducting Tunnel Junction) is a detector for neutrino decay search.
It is composed of Superconductor/Insulator/Superconductor. Trapped quasi-particles near insulator film by Al layer cause back tunneling. Nb/Al-STJ has a trapping gain about 10.
FD-SOI MOSFET
At low temperature, the threshold voltage of FD-SOI-MOSFET shifts larger and Ids increase. As far as we operate suitable voltage, it does not matter. We develop cryogenic amplifier using FD-SOI MOSFET.
Operation at low temperature (<3K)
Fast response speed (width of signal <10μs)
Low power consumption
  Cooling power of our refrigerator are 250mW at 4.2K and 100μW at 300mK.
Requirement for Cryogenic Amplifier
COBAND experiment is aiming to measure neutrino decay photons for a decision of neutrino masses.
The cryogenic operational amplifier using FD-SOI MOSFET is being developed.
1. COBAND Experiment
2. Development of Cryogenic SOI Amplifier
Nb
Al
SiO2
Size : 10μm×10μm ~ 200μm×200μm
~400nm
Nb/Al-STJ
by neutrino oscillation experiments.
,e
Rocket experiment
  Aiming at a sensitivity to 1014 years for the neutrino lifetime
  The diffraction grating covers .
  We count number of photons inputted the 50×8 array of pixels respectively and measure the energy spectrum.
DAQ
Altitude 200～300km
Measure time 200sec
Pixels Nb/Al-STJ
Introduction of Cryogenic Amplifier
Nb/Al-STJ has leakage currents from thermal excitations and imperfect junctions by processing three-layer. Requirement for leakage current in Nb/Al-STJ is smaller than 100pA and the requirement is already achieved.
However we have not been able to detect the far-inferred single photon yet, because of the large noise from the refrigerator’s readout line. We consider amplifying the STJ signal by cryogenic amplifier placed near STJs.
STJ size | @300mK
50μm✕50μm | 224±29pA
20μm✕20μm | 39±13pA
10μm✕10μm | 14±7pA
STJ size | 
50μm✕50μm | 224±29pA
20μm✕20μm | 39±13pA
10μm✕10μm | 14±7pA
FD-SOI(Fully Depleted-Silicon On Insulator) MOSFET is a transistor under SOI process with a nano-channel layer.
Low power consumption
Suppress charge-up of the body
A group of JAXA/ISAS reported working the FD-SOI MOSFET at 4K.
※ T. Wada et al., J. Low. Temp. Phys. 167, (2012) 602
BOX SiO2
Substrate
Channel length : L
Channel width : W
～50nm
Ids-Vds Curve (Vgs = 2.0V)
Increasing drain current because of the high mobility
Vds[V]
Ids[μA]
Drifting the threshold
Ids-Vgs Curve (Vds = 1.8V)
Vgs[V]
Ids[μA]
SOI-STJ5
Buffering Stage Source Follower Circuit
Improvement of frequency band
Amplifying Stage Op-Amp with Negative Feedback
Lowering input impedance
Bias Circuit
Current Mirror Circuit
Cope with array of detector
Applying Iref=10μA, We observe Idd=40μA and Iss=-50μA.
signal
pedestal
output
>
mV✕μs
Failed Test of Charge Amplification
  The large current is coursed by drain avalanche when |Vgs|<|Vds| and |Vds|>1V, since carriers have high mobility at low temperature. Simulating operation points at all MOSFETs in SOI-STJ5, I located MOSFETs working within drain avalanche-area in bias circuit.
N channel
W/L=190μm/20μm
Assessment of SOI-STJ5 without Bias Circuit
Iref
Iref
Iref
2Iref
Iref
Idd
Iss
Vdd=1.5V
Vss=-1.5V
10mV
100μs
Qin
404fC
200fC
188fC
40fC
50μs
signal
50μs
pedestal
  Amplifying stage, buffering stage, the feedback resister and the feedback capacitor are bonded each other by Al wire.
  Applying Irefa=-10μA, Ireft=-2μA and Irefb=-20μA, We observe Idd=60μA and Iss=-28μA.
  The circuit works correctly at 3K much as measurement at room temperature.
    Magnitude of output signal Vpp～ 46mV (Qin=404fC)
    Gain～123mV/pC
    Equivalent input noise charge σQ0～5.5fC
Output signals @ 3K
3. Test of the Cryogenic Amplifier
The pulse-height distribution
when integration time is 50μs.
Gain
Chart: 
| 404 | 188 | 40 | 200
Vpp | 49.9355 | 22.9862 | 4.7558 | 23.7788
Chart: 
| 404 | 188 | 40 | 200
Vpp | 49.9355 | 22.9862 | 4.7558 | 23.7788
Chart: 
| 404 | 188 | 40 | 200
sigma | 7.6516 | 6.3774 | 6.0323 | 5.8548
Chart: 
| 404 | 188 | 40 | 200
sigma | 7.6516 | 6.3774 | 6.0323 | 5.8548
Equivalent Input Noise Charge
Amp.IN [μV]
time [μs]
time [μs]
SOISTJ4 Output
70
60
50
40
1600
1200
800
400
0
-80
0
-40
40
-80
0
-40
40
~18μV
~1.2mV
SOISTJ4 Input
Amp.OUT [μV]
SOI-STJ4
SOI-STJ4 is common source amplifier.
SOI-STJ4 made a success to amplify the STJ signal for the first time! It has a gain around 64.
3He Sorption Refrigerator
Conducting a test at low temperature, SOI-STJ placed on the lowest stage.
4. Summary
  SOI-STJ4 succeeded amplifying the STJ signal.
  SOI-STJ5 w/o bias circuit works as intend at low temperature.
  SOI-STJ5 w/o bias circuit has a gain around 123mv/pC.
Using 300fF or 60fF, we can detect a STJ signal for a visible single-photon.
  Equivalent input noise charge is about 5.5fC.
  SOI-STJ6 was designed to have higher gain.
  The two-steps SOI-STJ6 was designed to obtain 30～40mV output signal at a STJ signal for a far-infrared single photon.
  Amplifier stage of SOI-STJ6 has a higher gain.
  4 patterns for feedback capacitances
    3pF
    300fF
    60fF
  We designed two-steps amplifying SOI amplifier using SOI-STJ6 amplifier stage and SOI-STJ4 circuit. The two-steps SOI-STJ6 will obtain output signal magnitude about 30～40mV at a STJ signal for a neutrino decay single-photon in λ=50μm.
Design of SOI-STJ6
Pulse-Height @ 3K