## Slide 1: 宇宙背景ニュートリノ崩壊探索ロケット実験設計と検出器開発
武内勇司 (筑波大)
Dec. 7, 2013
ニュートリノフロンティア研究会
＠クロス・ウェーブ府中

## Slide 2: Collaboration Members
As of Dec. 2013
Japan Group
Shin-Hong Kim, Yuji Takeuchi, Kenji Kiuchi, Kazuki Nagata,
Kota Kasahara, Tatsuya Ichimura, Takuya Okudaira, Masahiro Kanamaru,
Kouya Moriuchi, Ren Senzaki (University of Tsukuba),
Hirokazu Ikeda, Shuji Matsuura, Takehiko Wada (JAXA/ISAS),
Hirokazu Ishino, Atsuko Kibayashi, Yasuki Yuasa(Okayama University),
Takuo Yoshida, Shota Komura, Ryuta Hirose(Fukui University),
Satoshi Mima (RIKEN),
Yukihiro Kato (Kinki University) ,
Masashi Hazumi, Yasuo Arai (KEK)
US Group
Erik Ramberg, Mark Kozlovsky, Paul Rubinov, Dmitri Sergatskov,
Jonghee Yoo (Fermilab)
Korea Group
Soo-Bong Kim (Seoul National University)

## Slide 3: Cosmic neutrino background (CB)
CMB
CB

## Slide 4: Motivation
Search for in cosmic neutrino background (CB)
  Direct detection of CB
  Direct detection of neutrino magnetic dipole moment
  Direct measurement of neutrino mass:
Aiming at sensitivity of detecting from decay for
  SM expectation
  Current experimental lower limit
  L-R symmetric model (for Dirac neutrino) predicts down to for - mixing angle

## Slide 5: Neutrino Magnetic Dipole Moment
LRS: SU(2)LｘSU(2)RｘU(1)B-L
SM: SU(2)Lｘ U(1)Y
Suppressed by , GIM
Suppressed only by
1026 enhancement to SM
Neutrino magnetic moment term
PRL 38,(1977)1252, PRD 17(1978)1395

## Slide 6: Photon Energy in Neutrino Decay
m3=50meV
m1=1meV
m2=8.7meV
E =4.4meV
E =24meV
Sharp Edge with 1.9K smearing
Red Shift effect
dN/dE(A.U.)
distribution in
meV]
From neutrino oscillation
From CMB fit (Plank+WP+highL+BAO)
50meV<<87meV, 14~24meV
51~89m
E =24.8meV

## Slide 7: Backgrounds to CB decay
AKARI
COBE
Zodiacal Light
Zodiacal Emission
Galaxy evolution model
Galactic dust emission
Integrated flux from galaxy counts
CMB
Sharp edge with 1.9K smearing and energy resolution of a detector(0%-5%)
Red shift effect
Expected spectrum
,
CIB (fit from COBE data)
CB decay
ニュートリノ崩壊光(, を仮定)の~3x104倍の宇宙赤外線背景放射(CIB)
更に黄道光がCIB観測データ(COBE)の約20倍
dN/dE(A.U.)

## Slide 8: Neutrino lifetime lower limit from AKARI data
x1012 yr
Fit CIB data to spectrum expected from decay assuming all contribution to CIB is only from decay
lifetime lower limit as a function of
Published in Jan. 2012
AKARI CIB data after subtracting foregrounds
and distant galaxies
Best fit spectrum from CB decay

## Slide 9: Detector requirements
Requirements for detector
  Continuous spectrum of photon energy around (, far infrared photon)
  Energy measurement for single photon with better than 2% resolution for to identify the edge spectrum
  Rocket and satellite experiment with this detector
Superconducting Tunneling Junction (STJ) detectors in development
  Array of 50 Nb/Al-STJ pixels with diffraction grating covering
    For rocket experiment aimed at launching in 2016 in earliest, aiming at improvement of lower limit for by 2 order
  STJ using Hafnium: Hf-STJ for satellite experiment (after 2020)
    : Superconducting gap energy for Hafnium
    for 25meV photon: if Fano-factor is less than 0.3

## Slide 10: STJ(超伝導トンネル接合）検出器
上下の超伝導電極間に電位差を与える
放射線(光)によって励起された準粒子がトンネル電流として観測
Superconducting Tunnel Junction
超伝導体 / 絶縁体 / 超伝導体のジョセフソン接合素子

## Slide 11
STJのエネルギー分解能
発生する準粒子の個数のゆらぎがエネルギー分解能の限界を決める
超伝導ギャップエネルギーが小さいものが有利
 | Si | Nb | Al | Hf
Tc[K] |  | 9.23 | 1.20 | 0.165
Δ[meV] | 1100 | 1.550 | 0.172 | 0.020
Hc[G] |  | 1980 | 105 | 13
Δ: バンドギャップエネルギー
F: fano factor
E: 放射線のエネルギー
Hfを用いた場合の発生準粒子数 N=25meV/1.7Δ=735個
  ΔE/E < √ F/√N= √ F/√735=3.7 √ F % ＠25meV
  Fano factor <0.3なら分解能2％を達成可能
Tc :相転移温度
超伝導膜に用いた金属のTc（相転移温度）の1/10程度で安定動作
Hc :臨界磁場
STJのエネルギー分解能
Nbの場合の発生準粒子数 N=25meV/1.7Δ=9.5個
Energy resolution はないがphoton counting は可能
Notes: 11

## Slide 12: STJ検出器の性能評価法
STJの電流電圧(I-V)特性を測定
STJの超伝導転移，ジョセフソン接合の有無，リーク電流，エネルギーギャップなど素子の性能がわかる
ジョセフソン電流は磁場を印加して抑制

## Slide 13: STJバックトンネリング増幅効果
放射線(光子）
トンネルバリアの近傍の準粒子は，次々とトンネル効果を引き起こし電荷を増幅する
  トンネルバリアの近傍の準粒子の存在確率を上げるためトラップ層を置く
  Nb/Al-STJ Nb(200nm)/Al(10nm)/AlOx/Al(10nm)/Nb(100nm)
    近接効果によりAlの超伝導転移温度はNbの転移温度に近づく
増幅効果 2～200倍
Nb
Al
Nb
Al

## Slide 14
FIR photon spectroscopy with diffraction grating + Nb/Al-STJ array
  Diffraction grating covering (16-31meV)
Array of Nb/Al-STJ pixels: 50()x8()
  We use each Nb/Al-STJ cell as a single-photon counting detector with extremely good S/N for FIR photon of
  for Nb: if consider factor 10 by back-tunneling
  Expected average rate of photon detection is ~350Hz for a single pixel
Need to develop ultra-low temperature (<2K) preamplifier
  In collaboration with Fermilab Milli-Kelvin Facility group (Japan-US collaboration: Search for Neutrino Decay)
  SOI-STJ in development with KEK
Nb/Al-STJ array
Assuming for STJ response time, requirements for STJ
Leak current <0.1nA
Need T<0.9K for detector operation
 Need to 3He sorption or ADR for the operation

## Slide 15: Feasibility of FIR single photon detection
Assume typical time constant from STJ response to pulsed light is ~1μs
Assume leak current is 0.1nA
Fluctuation due to electron statistics in 1μs is
While expected signal charge for 25meV are
(Assume back tunneling gain x10)
  More than 3sigma away from leakage fluctuation
Requirement for amplifier
    Noise<16e
    Gain: 1V/fC  V=16mV

## Slide 16: JAXA Rocket Experiment for Neutrino Decay Search
Focal length 1m
JAXAのロケット実験
  ロケットで高度200km~300kmまで上昇．約5分の観測
  検出器，光学系，冷凍機のR&D完了から2年程度で打ち上げ可能 (2016年~)
  (16-31meV)の範囲で連続スペクトラムを測定(回折格子で50分割)
    100μm x 100μm x 50x8 array

## Slide 17: Cosmic Infrared Background measured by COBE and AKARI
COBE: M. G. Hauser et al. Astrophys. J. 508 (1998) 25, D. P. Finkbeiner et al. Astrophys. J. 544 (2000) 81.
AKARI: S. Matsuura et al. Astrophys. J. 737 (2011) 2.
at λ＝50μm
ロケット実験観測範囲 ４0μm ～８０μm
AKARI
COBE
Zodiacal Light
Zodiacal Emission
Galaxy evolution model
Galactic dust emission
Integrated flux from galaxy counts
CMB
Zodiacal Emission
~500nW/m2/sr
CIB (COBE)
~30nW/m2/s
Neutrino decay
for
~30nW/m2/s
for
~1pW/m2/s

## Slide 18
前景放射強度(黄道光): ~500nW/m2/sr at λ＝50μm
Pixelあたりの立体角:
望遠鏡口径: S=π x 0.0752 m2
Pixelあたりの前景放射レート
Measurements for 200s x 50 pixel x 8列
→ N=28M events / 50x8 pixels
Sensitivity to detecting an edge spectrum
→ 0.19nW/m2/sr
yr (95%CL)の寿命下限設定が可能
JAXA Rocket Experiment for Neutrino Decay Search
Event Rate and expected Lifetime Limit
dN/dE
E

## Slide 19: Summary
宇宙背景ニュートリノ崩壊探索実験ためのロケット実験を提案
  高度200kmで約5分の遠赤外域分光測定
  Nb/Al-STJ arrayと回折格子の組み合わせによる波長の連続スペクトラム
  yr (95%CL)の寿命下限設定(現在の下限値を1~2桁改善)
R&D
  Nb/Al-STJによる25meV(50μm)フォトンの1光子計数
    leakage <0.1nA, 受光面積100μmx100μm/pixel, back-tunneling gain>10
  そのための超低ノイズアンプ(極低温アンプnoise <16e, gain>1V/fC): SOI-STJなど
  分光素子・光学系の設計:望遠鏡口径 15cmΦ, 焦点距離1m
  ロケット搭載クライオスタットの設計 (<0.9K)
    LHe減圧(1.8K)＋3He sorption
  DAQ

## Slide 20: Backup

## Slide 21: Energy/Wavelength/Frequency

## Slide 22: Feasibility of VIS/NIR single photon detection
Assume typical time constant from STJ response to pulsed light is ~1μs
Assume leakage is 160nA
Fluctuation from electron statistics in 1μs is
While expected signal for 1eV are
(Assume back tunneling gain x10)
  More than 3sigma away from leakage fluctuation

## Slide 23: Nb/Al-STJによる可視光分光
国立天文台
  λ=475nｍ