## Adopting ATLAS DB to Run IIb Silicon Sensor

The sensor DB, so far, was based on Excel, since Hamamatsu uses Excel as default.

If we are to use ATLAS DB, we require anyway to adopt the test data structure to it (Excel itself does not fit to ATLAS DB). Under this condition and since sensor delivery is due in a month, we have not enough time to perform a big revision of the orginal ATLAS DB: we need to fix the data structure as soon as possible.

The general procedure of data uploading would be

1. Hamamatsu or Tsukuba/Korea/FNAL

- registers the sensor

- uploads manufacturer data

The both can be done by preparing a text (an example is in this note) and access to the DB via Java script through Web.

2. Testing Institute

- uploads the test data of the registered sensors

This also can be done via Web.  Skelton texts are in this note.

3. Shipping

Shipping sensors is handled in ATLAS by DB as well. One requires to send “Receive” data. Uploading test data for not-”received” sensors is not permitted.

4. Final qualification

Certain test fields (Leak current at 150V and 350V, visual inspection) are checked by DB and final qualification is provided automatically. (This means everybody needs to upload data as requested)

The ATLAS DB adoption to CDF would involve:

- Trim off unnecessary parts (not now?)

- Tune parameters (e.g. strip number is not integer, 150 and 350V are not suitable)

- Modify Java scripts

DATA UPLOAD in text format

%NEWTEST

SERIAL NUMBER: S0012

TEST MADE BY: KH

LOCATION NAME: Tsukuba

TEST DATE:5/20/2003

PASSED: yes

PROBLEM: none

Run number: 03

ATLAS　Integer[1,1536]

－＞　CDF string

Manufacture Data:

%ITEM

SERIAL NUMBER	S0012

Mfr serial number	STN39189-00012

%TEST

TEST DATE (DD/MM/YYYY)	10/03/2005

PROBLEM		NO

PASSED		YES

Run number	20220900200016

%DATA

TEMPERATURE (C)		27

I_LEAK500V (microA)		0.088

I_LEAK700V (microA)		0.126

Substr Origin		003

Substr Orient		111

Substr R Upper (kOhm.cm)	8

Substr R Lower (kOhm.cm)	4

Thickness (micron)		289

Vdep (V)			65

R Bias Upper (MOhm)		1.62

R Bias Lower (MOhm)		1.29

%COMMENT

%DEFECT

#DFEFCT NAME	FIRST CHANNEL	LAST CHANNEL

Implant-Break

Implant-open

Implant-short

Resistor-Break

Oxide-Punchthrough

Short

Open

%RAWDATA

Filename	IVS0012_001.dat

#IV

10	35

20	46.7

…

1000	200

Filename	CVS0012_001.dat

#CV

10	O.L.

15	O.L.

20	2590

25	2230

…

300	1400

# Text boxes

This part (=header) is mandatory

READ LINES: necessary

GREEN LINES: optional

One or mutliple sets of text describing the test results. Possible sets are listed below.

# full depletion voltage

%DetVDep

TEMPERATURE: 	21

VDEP: 		150

Radiation dose:	0

# defect channels

%DEFECT

DEFECT NAME: Implant-open

FIRST CHANNEL: RU21

LAST CHANNEL: RU21

url:

# Web link to data

%Web_link

DESCRIPTION: AC scan

URL: http://hep-www….

# comment

%Comment

This sensor is intensively probed and there are many probe traces.

# visual inspection

%VisInspec

Large crack. Photos in

http://… /scratch.gif

DEFECT name:

Open

Short

Oxide-Punchthrough

Pinhole

Resistor-Break

Implant-Short

Implant-Open

#create file and store rawdata

%Test_Rawdata

FILENAME: IVS0012_03.dat

#IV

10	35

20	46.7

….

30	52.9

40	57.4

CV rawdata

There are many others, but the above are enough.

IV rawdata

List of dead channels